## Slide 1
Compound identification in MS metabolomics
NEXS, University of Copenhagen 16th February 2017
Jan Stanstrup
jan.stanstrup@regionh.dk
stanstrup@gmail.com
http://stanstrup.github.io
@JanStanstrup

## Slide 2: Why is identification important?
No ID  no biological context
Database hits are not enough!
Most time-consuming part of the whole pipeline
Notes: Where we are in the pipeline
Why ID important
ID and inter together.
That is because they are very much tied in to each other
Therefore I think that everybody - even if you are working mainly on the biological aspects on the study – should have some idea how ID is done

## Slide 3: Agenda
The molecular formula
From mass alone
Exercise 1
How to know if a molecular formula is possible (nitrogen rule & DBE)
Using isotopic pattern
Using isotopic fine pattern
Ion charge
Automatic decomposition
The pseudo-molecular ion
MS1: Adducts and In source fragmentation
Automatic deconvolution and annotation
Compound candidates from databases
Compound databases
Spectral databases
Fragmentation pattern
The manual way
Exercise 3
Retention time
Is it useful?
How can we use it?
How sure are you?
MSI levels
Are MSI levels all we need to know?
In silico tools

## Slide 4: Finding the molecular formula

## Slide 5: Molecular formula: Mass alone – Exercise 1
 | Mass
H | 1.0078
C | 12.0000
N | 14.0031
O | 15.9949
P | 30.9738
S | 31.9721
Cl | 34.9689
Mass = 46. What can it be?

## Slide 6: Molecular formula: Nitrogen rule
For organic compounds containing exclusively H, C, N, O, Si, P, S, and the halogens:
odd nominal mass  odd number of N atoms
even nominal mass  zero or even number of N atoms
N.B.:
Reverses for +H and –H charged compounds!
Does NOT reverse for electron impact (i.e. classical GC since only an electron is lost)
Only works for small molecules (the non-integer part of masses will add up)
http://fiehnlab.ucdavis.edu/projects/Seven_Golden_Rules/Nitrogen_Rule
Notes: No clever reason why this is like this
Consequence of the number of bonds the different atoms make

## Slide 7: Molecular formula: Double bond equivalent
DBE = 1 !
Double bond equivalent (DBE) == Ring Double Bond Equivalents (RDBE) ==
Degree of unsaturation (UN, DoU) == Pi Bonds or Rings (PBoR)
Fiehn regarding why DBE is misleading: http://fiehnlab.ucdavis.edu/projects/Seven_Golden_Rules/Ring-Double-Bonds
For molecules containing only carbon, hydrogen, monovalent halogens, nitrogen, and oxygen:
C = number of carbons, H = number of hydrogens, X= number of halogens and N = number of nitrogens.
All other atoms are ignored.
Double bonds  +1 DBE
Triple bonds  +2 DBE
Rings  +1 DBE
Benzene rings  +4 DBE
Notes: Cannot have a negative number of double bonds
Cannot have half a double bond
Hint of benzene

## Slide 8: Molecular formula: Isotope pattern
https://commons.wikimedia.org/wiki/File:Nucleosynthesis_periodic_table.svg
Isotopes: atom with same number of protons and electrons, but different number of neutrons.
The mass of an atom is less than the sum of the parts (up to iron). Think E=mc2. This 'missing mass' is known as the mass defect, and represents the energy that was released when the nucleus was formed
The change in mass defect caused by adding neutrons is different for each atom.
On earth the abundance of isotopes are more or less fixed.  Can be exploited for identification.

## Slide 9: Molecular formula: Isotope pattern
 | Mass | Rel. abundance
H | 1.0078 | 0.999885
 | 2.0141 | 0.000115
C | 12.0000 | 0.9893
 | 13.0033 | 0.0107
N | 14.0031 | 0.99636
 | 15.0001 | 0.00364
O | 15.9949 | 0.99757
 | 16.9991 | 0.00038
 | 17.9992 | 0.00205
P | 30.9738 | 
S | 31.9721 | 0.9499
 | 32.9715 | 0.0075
 | 33.9679 | 0.0425
Cl | 34.9689 | 0.7576
 | 36.9659 | 0.2424
C6H5Cl
http://www.alchemistmatt.com/mwthelp/isotopicdistribution.htm
http://www.chem.uoa.gr/applets/AppletMS/Appl_Ms2.html
0.98936 • 0.9998855 • 0.7576 = 0.7098
6 • (0.98935 • 0.0107 • 0.9998855 • 0.7576) +
5 • (0.98936 • 0.9998854 • 0.000115 • 0.7576)
= 0.04647
(difference to table due to differences in abundances in sources data)
+1
+2
+3
monoisotopic mass
Notes: Which means if we propose a formula for or our unknown we can check if the experimental isotopic pattern fit the theoretical pattern that we can calculate

## Slide 10: Molecular formula: Isotopic fine pattern
+1 Isotope
+2 Isotope
360.1842-360.1905 = -0.0063
 15N
13C
Notes: So the last calculation we did before with the carbon and hydrogen isotope would actually be two different mass peaks at very slightly different mass.

## Slide 11: Molecular formula: Isotopic fine pattern
+1 Isotope
+2 Isotope
15N
33S
13C
2H
34S
13C,15N
13C,33S
18O
13C, 13C
If you have an orbitrap check out exercise 2!
Notes: So the last calculation we did before with the carbon and hydrogen isotope would actually be two different mass peaks at very slightly different mass.

## Slide 12: Molecular formula: Ion charge
What we measure is mass devided by the charge (m/z)
Methionine  C5H11NO2S  mass = 149.0510
If single charged positive mode [M+H]+:
m/z =
If double charged negative mode [M-2H]-2:
m/z =
Most small molecules are usually present only as single-charged species
Larger molecules (>500) often also form species with multiple charges
Very large molecules (>>1000) can be present primarily as species with multiple charges
Mass of a proton (H+)

## Slide 13: Molecular formula: Ion charge
The isotopic pattern can tell us the charge
Methionine single-charge isotopes peaks:
Ion Species | Isotope | Calculation of m/z
[M+H]+ | [M]+ | (149.0510 + 1.0073)/1 = 150.0583
[M+H]+ | [M+1]+ | (149.0510 + 1.0073 + 1.0033)/1 = 151.0616
[M+H]+ | [M+2]+ | (149.0510 + 1.0073 + 1.0033*2)/1 = 152.0649
= 12C and 13C difference.
Estimation only! Real mass is an ”average” of the contributing isotopes.
Difference ~ 1 Da

## Slide 14: Molecular formula: Ion charge
The isotopic pattern can tell us the charge
Methionine double-charged isotopes peaks:
Ion Species | Isotope | Calculation of m/z
[M+2H]2+ | [M]+ | (149.0510 + 1.0073*2)/2 = 75.5328
[M+2H] 2+ | [M+1]+ | (149.0510 + 1.0073*2 + 1.0033)/2 = 76.0345
[M+2H] 2+ | [M+2]+ | (149.0510 + 1.0073*2 + 1.0033*2)/2 = 76.5361
Difference ~ 0.5 Da

## Slide 15: Molecular formula: Automatic decomposition
http://predret.org/tools/mass-decomposition/
Kind T, Fiehn O. BMC Bioinformatics. 2007 Mar;8(1):105.
Notes: 7 golden rules from Oliver Fiehn’s group. Must read paper.

## Slide 16: Molecular formula: Automatic decomposition

## Slide 17: Molecular formula: Automatic decomposition

## Slide 18: Finding the pseudo-molecular ion
Notes: Need to make sure that we are look at the so called pseudo-molecular ion
So let is take a look at what the problem is

## Slide 19
Ionization in the ESI source. Some in-source fragmentation takes place (green here).
Everything passes the quadrupole
Collision cell is ”off”
TOF separates by m/z
Additional info from fragmentation: MS1 (Q-TOF)
Notes: Only ionized by adding or removing a hydrogen.
There are other things than fragments that can cause additional peaks from the same compound  adducts

## Slide 20
Finding the molecular ion: Adducts
Usually caused by molecules being charge by combining with a charged species other than H (e.g. Na+, K+, Cl-).
Neutral adducts also exist (e.g. formic acid, acetone, sodium formate, NaCl)

## Slide 21
Finding the molecular ion: Adducts

## Slide 22
Finding the molecular ion: Adducts
[M+Na+]+
[M+K+]+
[2M+H+]+
[2M+Na+]+
[2M+K+]+
[2M+NH4+]+
[2M+Fe3+-2H-]+
Notes: There is not the most common adducts that would be chloride - or at least they are very small – but we see these other adducts… 
Remember this is MS1. so also coeluting compounds
Doing this manually is a very tedious process

## Slide 23
Finding the molecular ion:
Adducts and fragments with CAMERA
Fragment lists @ https://github.com/stanstrup/chemhelper/tree/master/inst/extdata
mzmine2xcmsSet @ https://github.com/stanstrup/chemhelper
mz | rt | isotopes | adduct | pcgroup
117.0545 | 1.38 |  |  | 878
144.1019 | 1.41 |  |  | 878
163.0604 | 1.35 |  | [M+H-Leu]+ 293.148 | 878
276.1444 | 1.45 |  | [M+H-H2O]+ 293.148 | 878
280.1393 | 1.41 |  | [M+H-CH2]+ 293.148 | 878
294.1550 | 1.41 |  | [M+H]+ 293.148 | 878
295.1582 | 1.41 |  |  | 878
119.0491 | 1.40 |  | [M+H-NH3-HCOOH]+ 181.074 | 879
123.0440 | 1.40 |  | [M+H-NH3-COCH2]+ 181.074 | 879
136.0756 | 1.40 | [29][M]+ | [M+H-HCOOH]+ 181.074 | 879
137.0790 | 1.40 | [29][M+1]+ |  | 879
147.0441 | 1.40 |  | [M+H-NH3-H2O]+ 181.074 | 879
165.0547 | 1.40 | [65][M]+ | [M+H-NH3]+ 181.074 | 879
166.0581 | 1.40 | [65][M+1]+ |  | 879
182.0812 | 1.40 | [85][M]+ | [M+H]+ 181.074 | 879
183.0841 | 1.40 | [85][M+1]+ |  | 879
184.0854 | 1.40 | [85][M+2]+ |  | 879
204.0633 | 1.40 |  | [M+Na]+ 181.074 | 879
363.1554 | 1.40 |  | [2M+H]+ 181.074 [4M+2H]2+ 181.074 | 879
120.0515 | 1.40 |  |  | 880
122.0792 | 1.40 |  |  | 881
123.0552 | 1.40 |  |  | 882
322.0772 | 1.40 |  |  | 882
348.0708 | 1.40 |  | [M+H-COCH2]+ 389.074 | 882
428.0367 | 1.34 |  | [M+K]+ 389.074 | 882
124.0448 | 1.40 |  |  | 883
126.0298 | 1.40 |  | [M+H-gluc-(H2O)2]+ 337.065 | 884
152.0097 | 1.40 |  | [M+H-NH3]+ 168.029 | 884
169.0357 | 1.40 | [73][M]+ | [M+H]+ 168.029 | 884
170.0390 | 1.40 | [73][M+1]+ |  | 884
171.0402 | 1.40 | [73][M+2]+ |  | 884
185.0308 | 1.42 |  |  | 884
338.0683 | 1.40 |  | [M+H]+ 337.065 | 884
CAMERA says this is one compounds
Notes: So now help arrives

## Slide 24
Finding the molecular ion:
Adducts and fragments with CAMERA

## Slide 25
Finding the molecular ion:
Adducts and fragments with CAMERA

## Slide 26
Finding the molecular ion:
Adducts and fragments with CAMERA

## Slide 27: Using the fragmentation pattern

## Slide 28
Ionization in the ESI source. Some in-source fragmentation takes place (not shown).
Only selection ion passes the quadrupole (red). Careful: Isolation window is usually 1+ Da.
  MSn-like spectra by fragmenting a known fragment (in-source fragmentation)
Fragmentation in the collision cell
TOF separates by m/z
Additional info from fragmentation: MS2 (Q-TOF)
Notes: Different energies can give different fragments.
Orbitraps have several fragmentation modes

## Slide 29
Interpreting fragmentation data: The manual way
-H2O
-CH4S
-HCOOH

## Slide 30
Interpreting fragmentation data: The manual way
Keller BO, Sui J, Young AB, Whittal RM. Anal Chim Acta. 2008;627(1):71–81.
Notes: This is also the list you can look at when you are looking for adducts

## Slide 31
Interpreting fragmentation data: The manual way
Pretsch, Buļhlmann & Badertscher. Structure Determination of Organic Compounds: Tables of Spectral Data.

## Slide 32
Interpreting fragmentation data: The manual way
-H2O
-CH4S
-HCOOH
C5H11NO2S
-NH3
C8H6O
DBE = 6
 Methionine!
-HCOOH

## Slide 33
Interpreting fragmentation data: The manual way
– the good
-H2O
-CH4S
-CO
-HCOOH
-phenylacetyl
-NH3
-HCOOH
(
)
Notes: This is where biology and identification intersects
Probably this compound was created by a reaction between methionine and Phenyl acetate.
So there used to be an acid group here which made this reaction possible.

## Slide 34
Interpreting fragmentation data: The manual way
– the ugly
Anal. Methods, 2014, 6, 8915-8923

## Slide 35
Open ”Exercise (20120106-005).mzData” in MzMine
Go to spectra 396 @ ~1.45 min. This is MS1. Not MS2.
What is the pseudo-molecular ion [M+H+]+?
What is the charge?
What is the possible/reasonable molecular formula at this point?
Interpreting fragmentation data: Exercise 3 – part 1

## Slide 36
Open ”Exercise (20120106-005).mzData” in MzMine
Go to spectra 396 @ ~1.45 min. This is MS1. Not MS2.
What is the pseudo-molecular ion [M+H+]+?
What is the charge?
What is the possible/reasonable molecular formula at this point?
Annotate as many ions as possible
What is the molecular fomula?
What is the compound?
Interpreting fragmentation data: Exercise 3 – part 2

## Slide 37: Finding plausible compound candidates from databases

## Slide 38
Compound databases
Global
  Indiscriminant selection of compounds
  Large (tens of millions)
  Contains the structure of compounds. Little other info
Focused
  Biology specific
  Compound class specific
  Relatively small (tens of thousands)
  Can contain additional contextual information
Spectral databases
  Indiscriminant selection of compounds
  Relatively small (tens of thousands)
Contains authentic spectra of compounds
Compound and spectral databases
Notes: Not because you should assume that a hit in the database means you have identified your compound but 
Easier to confirm a hypothesis than to generate one.
Be careful: spectra from different machines are not identical

## Slide 39
HMDB (hmdb.ca)
  My compound ID (www.mycompoundid.org)
METLIN (metlin.scripps.edu)
Lipidmaps (www.lipidmaps.org)
Phenol-explorer (phenol-explorer.eu)
ChEBI (www.ebi.ac.uk/chebi/)
Chemspider (www.chemspider.com)
PubChem (pubchem.ncbi.nlm.nih.gov)
MassBank (www.massbank.jp)
mzCloud (https://www.mzcloud.org)
More in: Medina S et al. Trends in Analytical Chemistry The effects of the intake of plant foods on the human metabolome. Trends Anal Chem. 2013;52:88–99. http://dx.doi.org/10.1016/j.trac.2013.08.002
Compound and spectral databases

## Slide 40
Small human metabolites (41.993 metabolite entries)
Searches
  MS
  MS/MS
  compound
Metabocards
  Description of metabolite
  MS/MS spectra
  links to other databases
Extended by MycompoundID.com
  “Predicts” biological adducts
  Predicts MS spectra for the predicted compounds
Huan T, Tang C, Li R, Shi Y, Lin G, Li L. MyCompoundID MS/MS Search: Metabolite Identification Using a Library of Predicted Fragment-Ion-Spectra of 383,830 Possible Human Metabolites. Anal Chem. 2015;87(20):10619–26.
Compound and spectral databases: HMDB

## Slide 41
Compound and spectral databases: HMDB

## Slide 42
Compound and spectral databases: HMDB

## Slide 43
Most known compounds (>40 million structures)
Searches
  Name
  Formula
  Structure
Many name synonyms
An alternative is PubChem
Compound and spectral databases: ChemSpider

## Slide 44
Compound and spectral databases: ChemSpider

## Slide 45
Compound and spectral databases: ChemSpider

## Slide 46
Metlin (metlin.scripps.edu)
HMDB (hmdb.ca)
MassBank (www.massbank.jp)
MzCloud (www.mzcloud.org)
Compound and spectral databases: Spectral database

## Slide 47
Searches
  MS (possible to select adduct or parent ion)
  MS/MS
  Fragment
  neutral loss
  compound
Metabolites (242.766 metabolite entries)
MS/MS data high resolution
  same instrument
  many energies
  11.676 metabolites
Compound and spectral databases: METLIN

## Slide 48
Compound and spectral databases: METLIN

## Slide 49
40.000+ spectra from different instruments
Fragment search
m/z difference search
Compound and spectral databases: MassBank

## Slide 50
Compound and spectral databases: MassBank

## Slide 51: In silico prediction

## Slide 52
In-silico fragmentation
MetFrag (msbi.ipb-halle.de/MetFrag)
MetFusion (msbi.ipb-halle.de/MetFusion)
CFM-ID (cfmid.wishartlab.com) – “smarter” than MetFrag. Searches only HMDB/KEGG.
CSI:FingerID (www.csi-fingerid.org) – State of the art. Very computer intensive.
In-silico mass spectra
LipidBlast (fiehnlab.ucdavis.edu/projects/LipidBlast)
Automatic annotation
CAMERA (XCMS extension for adduct/fragment annotation)
Retention time prediction/mapping
PredRet (predret.org)
www.retentionprediction.org
In silico prediction: Mass spectra

## Slide 53
In silico prediction: CSI:FingerID

## Slide 54
In silico prediction: CSI:FingerID

## Slide 55
In silico prediction: CSI:FingerID
Notes: You can also do with MS1
Give you a hypothesis earlier in the game

## Slide 56
Search spectral databases AND compound databases
Combined score based on
  existing experimental spectra of similar compounds
  In-silico fragmentation of compounds in compounds database
Suggests fragmentation
In silico prediction: MetFusion

## Slide 57
In silico prediction: MetFusion

## Slide 58
In silico prediction: MetFusion

## Slide 59: Fragmentation is not everything

## Slide 60
STANDARDS STANDARDS STANDARDS
Retention time prediction/mapping
Quantitative Structure Retention Relationship (QSRR) models ->
  Based on modelling a large number of structural descriptors to the retention time
  Many many system specific models have been published.
In silico prediction: Retention time
Notes: You cannot have databases like for mass spectra

## Slide 61
Stanstrup, J., Gerlich, M., Dragsted, L. O., & Neumann, S. (2013). Metabolite profiling and beyond: Approaches for the rapid processing and annotation of human blood serum mass spectrometry data Metabolomics and Metabolite Profiling. Anal. Bioanal. Chem., 405(15), 5037–5048.
In silico prediction: Simple QSRR model

## Slide 62
STANDARDS STANDARDS STANDARDS
Retention time prediction/mapping
Quantitative Structure Retention Relationship (QSRR) models ->
  Based on modelling a large number of structural descriptors to the retention time
  Many many system specific models have been published.
www.retentionprediction.org
PredRet (predret.org)
In silico prediction: Retention time

## Slide 63
In silico prediction: Retention time with PredRet
Stanstrup, J., Neumann, S., & Vrhovsek, U. (2015). PredRet: Prediction of Retention Time by Direct Mapping between Multiple Chromatographic Systems. Analytical Chemistry.

## Slide 64
In silico prediction: Retention time with PredRet

## Slide 65
In silico prediction: Retention time

## Slide 66: So are you really really sure or just a little sure?

## Slide 67
Standard for reporting of identifications proposed by the Metabolomics Standards Initiative (MSI)
LEVEL I: Identified compounds
Two independent measures (eg. RT and m/z)
compared to an authentic standard
LEVEL II: Putatively annotated compounds
Physicochemical properties and/or spectral similarity with public/commercial spectral libraries
LEVEL III: Putatively characterized compound classes
physicochemical properties of a chemical class of compounds, or by spectral similarity to known compounds of a chemical class
LEVEL IV: Unknown compounds
Metabolomics. 2007;3(3):211–21.
Identification levels (MSI): AKA how sure are you?

## Slide 68
Q1: Given the information you have looked at what level of ID is this?
Q2: What do you need to do to get better ID?
Q3: Does MSI level I == 100 % sure ID?
  Other compounds could also have ~same RT and ~same spectra
Q4: Could ”100 % sure ID ” mean different things to different people?
  Positional isomers (especially lipids)
  Cis/trans
  Stereoisomers
Identification levels (MSI): Exercise 3 revisited

## Slide 69: Summary

## Slide 70
The mass and isotope pattern help you find the molecular formula Molecular formula of fragments and losses are also informative
Not all possible formula are valid compounds (nitrogen rule, DBE)
Adducts can help (or make it more difficult to) find the pseudo-molecular ion
Fragments give info on the structure of the compound
Compound databases show us what compounds are known
Spectral databases give us spectra of real compounds
In silico tools can help us when no real spectrum is available
It is crucial to report the level of certainly unambiguously
Summary: From features to compounds

## Slide 71: Recommendations
Start with low hanging fruits.
  Search databases first.
  Give up fast if not enough data or get more data (MSn) if possible/important. Accept that you won’t ID everything.
Find the pseudo-molecular ion before you try to ID.
Always check EIC before trying to ID a feature/fragment/adduct.
Don’t use the MSI levels blindly. Use good chemical sense and report uncertainty meticulously.
Remember: There is no substitute for authentic standard compounds. But they might not be enough!